DLD lab report 4
student number: 16329561

This lab we needed to simulate a car 4-bit value sensor which determines when the car should enter Eco-mode. The values, or minterms, for this are 0, 2, 5, 6, 9, 11. Thus we need to implement the following function:

F(w,x,y,z) = Σm(0,2,5,6,9,11)

For this, I used the Quine-McCluskey algorithm. After pairing the minterms together, I got 4 prime implicants and all of them were essentials. I had m(5), m(2,6), m(0,2) and m(9,11) which gives us at first:

F(w,x,y,z) = (w’xy’z)+(w’x’z)+(w’yz’)+(wx’z) but with the distributivity law we can reduce the expression to one with only 10 literals, as follow:
F(w,x,y,z) = w’(xyz+z’(x’+y))+(wx’z)
Giving this circuit:

W	X	Y	Z	F(W,X,Y,Z)
0	0	0	0	1
0	0	0	1	0
0	0	1	0	1
0	0	1	1	0
0	1	0	0	0
0	1	0	1	1
0	1	1	0	1
0	1	1	1	0
1	0	0	0	0
1	0	0	1	1
1	0	1	0	0
1	0	1	1	1
1	1	0	0	0
1	1	0	1	0
1	1	1	0	0
1	1	1	1	0